## Slide 1
TELECOM DIGITAL TWIN ARCHITECTURE
Digital Twin Adapters & Standards
How operator intent, ETSI TeraFlowSDN, ns-3 co-simulation and Ceragon microwave hardware work as one closed loop
Ceragon Networks · ETSI TeraFlowSDN research · Standalone & production hybrid architecture
Intent
Operator & SLA
SDN controller
ETSI TeraFlowSDN
Simulator
ns-3 discrete events
Hardware
Ceragon MH-T261
Notes: What are the adapters? Software translators that bridge the different timing, data formats and control protocols of the four parts of the twin. Standards: TM Forum TMF921, 3GPP TS 28.561, ITU-T Y.3090, ITU-T Y.3092, IETF RFC 8040 RESTCONF / RFC 7950 YANG 1.1, with ETSI TeraFlowSDN as the SDN controller. Closed-loop automation: every change is predicted in a discrete-event what-if run before it is actuated on hardware with a two-phase commit.

## Slide 2
THE PROBLEM
Four components, four languages, four clocks
1 µs
1 ms
1 s
1 min
1 h
1 day
Operating timescale (log)
Declarative intent
Natural language / JSON
minutes – days
SDN controller
Context DB · gRPC · CSPF
seconds
Discrete simulator
C++ event queue & packets
microseconds
Physical hardware
RESTCONF · PHY registers
sub-ms
Adapters translate both the protocol and the clock between neighbours.
Notes: In a telecom digital twin the components speak different languages and run on very different timescales. Adapters bridge that semantic and temporal gap. 1. Declarative intent (human operator / SLA): natural language or JSON, minutes to days. Example: 'Ensure URLLC latency < 1.5 ms and 99.999% availability during storms'. 2. SDN controller (ETSI TeraFlowSDN): Context DB, gRPC, CSPF; seconds (control plane). Data: device UUIDs, endpoints, topology graphs, TI-LFA backup paths. 3. Discrete simulator (ns-3 core): C++ event queue and packets; microseconds. Data: QueueDisc buffer drops, Wi-Fi EDCA AC_VO, link propagation delay. 4. Physical hardware (Ceragon MH-T261): RFC 8040 RESTCONF and PHY; sub-millisecond. Data: V-band 60.48 GHz, ACM MCS 0-9, RSSI/SNR, RF registers.

## Slide 3
ARCHITECTURE AT A GLANCE
Three adapters connect four domains in one loop
DIGITAL TWIN LAYER
PHYSICAL NETWORK LAYER
Layers follow ITU-T Y.3090; twin lifecycle follows 3GPP TS 28.561
Operator intent
SLA · natural language
TeraFlowSDN
ETSI OSG SDN controller
ns-3 simulator
discrete-event core
Ceragon MH-T261
60 GHz V-band radio
① Intent
TM Forum TMF921
② Simulation
TS 28.561 · Y.3092
③ Southbound
RFC 8040 RESTCONF · YANG 1.1
≈ 2 s
from SLA intent to a verified configuration change on the live radio
Notes: Intent adapter: translates natural-language or SLA bounds into TeraFlowSDN service and CSPF requests (TM Forum TMF921). Simulation adapter: syncs the live TFS graph into the ns-3 C++ discrete-event engine, scopes fidelity (tiers 1-5) and returns microsecond traces. Each simulation run is a 3GPP TS 28.561 NDT job over the ITU-T Y.3092 NDT-m interface (see the standards-alignment slide). Southbound driver: stages candidate-datastore diffs and runs two-phase commits to the Ceragon MH-T261 over RFC 8040 RESTCONF. ITU-T Y.3090 defines the layered twin reference model (physical network layer, digital twin layer, application layer). 3GPP TS 28.561 defines management of the network digital twin and its closed loop.

## Slide 4
STANDARDS
Each interface is anchored in an open specification
TM Forum TMF921
BUSINESS & SLA
Intent Management API
Operator states latency < 1.5 ms and availability. Intent state: Acknowledged → In evaluation → Compliant.
3GPP TS 28.561
TWIN LIFECYCLE
Digital twin management
Governs the 4-gate pre-flight check before any action reaches the network.
ITU-T Y.3090
ARCHITECTURE
Twin network architecture
Layered reference model; keeps the real-time shadow datastore in sync with the physical network.
ITU-T Y.3092
SIMULATION INTERFACE
NDT-m and NDT-p interfaces
Job control to the twin (NDT-m) and live state sync (NDT-p) for the what-if runs.
IETF RFC 8040 / 7950
HARDWARE INTERFACE
RESTCONF & YANG 1.1
Southbound to the MH-T261: candidate staging, diff validation, two-phase commit.
ETSI TeraFlowSDN
SDN CONTROL
Open-source SDN controller
gRPC microservices: Context :10010, Device :10020, Service/PCE :10030, Monitoring :10040.
Notes: TMF921: REST API for declarative intent and SLA expectations. The operator sets latency and availability without low-level scripts. 3GPP TS 28.561 (Management aspects of network digital twins): twin lifecycle and closed-loop control. In our platform it governs the 4-phase pre-flight gate: latency envelope, queue stability, hardware capability, spectral mask. ITU-T Y.3090 (Digital twin network: requirements and architecture): layered reference model and synchronisation between the physical network and the twin. Powers our real-time shadow datastore. ITU-T Y.3092 (09/2024, Digital twin for management and orchestration in IMT-2020 networks and beyond): defines NDT-m (management system to twin) and NDT-p (physical network to twin). Our simulation adapter uses NDT-m for what-if job control and NDT-p for live state sync. The IRTF NMRG network-digital-twin drafts describe a similar split but are research drafts. RFC 8040 / RFC 7950: RESTCONF over HTTP to YANG datastores. Southbound interface to the Ceragon MH-T261 (192.168.1.225:80). ETSI TeraFlowSDN: open-source SDN controller hosted by an ETSI Open Source Group (not a standard itself). Context (gRPC :10010), Device driver (:10020), Service/PCE (:10030), Monitoring telemetry (:10040).

## Slide 5
ADAPTER ② · TFS → NS-3
The simulation adapter mirrors the live network in ns-3
1 Reconcile
Pull the live 34-node graph and RF metrics (RSSI −58 dBm, MCS 8)
2 Scope
Fidelity governor trims the graph to the domain that matters
3 Perturb
Inject what-ifs: 3.5× traffic surge, ITU-R P.838 rain fade
4 Ingest
Stream queues, drops, latency and the NetAnim trace back to the twin
Chart: Governor resolution tiers (relative fidelity)
| T1 Macro-topology | T2 Queue dynamics | T3 Physical RF | T4 URLLC micro-packet | T5 Green energy
Fidelity | 25 | 55 | 75 | 95 | 20
34 → 23
nodes simulated when scoped to Tier 4 (URLLC)
≈ 1.15 s
per what-if run, instead of minutes for the full graph
Notes: Step 1: the adapter queries the TeraFlowSDN Context service for the active 34-node graph, link bandwidths and live Ceragon RF metrics. Step 2: the simulation resolution governor scopes the graph to the target domain instead of simulating all 34 nodes. Example: Tier 4 (URLLC micro-packet) uses 23 nodes and runs in about 1150 ms. Step 3: what-if stress is injected into ns-3: a 3.5x bulk traffic surge (bufferbloat) or ITU-R P.838 rain fade (ACM rate falls from 1 Gbps to 100 Mbps). Step 4: ns-3 simulates microsecond packet events on cersrv-029, writes /tmp/tsn_wifi_ceragon_anim.xml, and the adapter streams queues, drops and latencies back to the twin. Implementation: remote execution over SSH/JSON to ns-3.45 on cersrv-029, with an analytical local fallback for standalone mode. NetAnim AnimationInterface gives timeline playback (0.000-2.500 s) with 10 buffer slots and tail-drop alerts. Deterministic TSN mapping: 802.1Q PCP class 6 and EDCA AC_VO go to PfifoFast band 0.

## Slide 6
ADAPTER ② · STANDARDS ALIGNMENT
TFS ↔ ns-3 as a standard NDT job
TeraFlowSDN
NDT MnS consumer
Sim adapter + ns-3
NDT MnS producer
① createMOI (NDTJob)
capability: config verification · scope: 23-node Tier-4 graph
NDT-m
② Sync live state
topology and RSSI / MCS from TFS Context feed the twin model
NDT-p
③ NDTReport
predicted latency 1.12 ms · queue occupancy · drops
NDT-m
④ modifyMOI / deleteMOI
suspend or delete the job once the verdict is in
NDT-m
3GPP TS 28.561
HOW THE JOB RUNS
NDTFunction, NDTJob, NDTReport are managed objects
Created and changed with TS 28.532 MnS operations
Job carries run-time and precision limits
ITU-T Y.3092
WHICH INTERFACE
NDT-m: management ↔ twin (job control)
NDT-p: physical network ↔ twin (state sync)
Notes: This slide maps the simulation adapter onto two published specifications. It is the target alignment; confirm which messages the implementation already emits. 3GPP TS 28.561 (Management aspects of network digital twins) models the twin as managed objects: NDTFunction (the twin, with supportedNDTCapabilities and nDTFunctionScope), NDTJob (one simulation/emulation run for one scenario) and NDTReport (its output). They are created, modified and deleted with the generic TS 28.532 operations (createMOI, modifyMOIAttributes, deleteMOI, getMOIAttributes). TFS acts as the NDT MnS consumer. It creates an NDTJob whose nDTCapability is configuration verification and whose nDTJobSynchScope is the Tier-4 URLLC subgraph (23 nodes). ndtJobExecutionRequirements carries limits such as maximum run time and precision, which is where the fidelity governor's tier choice belongs. The simulation adapter plus ns-3 is the NDT MnS producer; it returns an NDTReport with predicted latency, queue occupancy and drops. After the verdict the job is suspended or deleted. ITU-T Y.3092 (09/2024, Digital twin for management and orchestration in IMT-2020 networks and beyond) names the interfaces: NDT-m between the management system and the twin, NDT-p between the physical network and the twin. Job control (1, 3, 4) runs over NDT-m; the live topology and RF state sync (2) is the NDT-p role, relayed here through TFS Context. The IRTF NMRG network-digital-twin drafts describe the same split informally, but they are research drafts.

## Slide 7
WHAT-IF IN PRACTICE
A storm on the V-band link, tested before it happens
Chart: Link rate (Mbps)
| Clear sky | Rain · MCS 0 floor | Rain · MCS 4 floor
Rate | 1000 | 100 | 500
Change the twin recommends
ACM floor
MCS 0
MCS 4
QoS queue
FIFO
PCP 6
Carrier
60.48 GHz
64.80 GHz
Predicted URLLC latency
1.12 ms of a 1.5 ms SLA
25% headroom → change passes the latency gate
Notes: Scenario values are the ones used in this deck: rain fade (ITU-R P.838) pushes adaptive coding and modulation down so the link rate falls from about 1 Gbps to 100 Mbps. Raising the ACM floor from MCS 0 to MCS 4 keeps at least 500 Mbps. The same candidate configuration also moves URLLC traffic into IEEE 802.1Q PCP class 6 (PfifoFast band 0) and retunes the carrier from 60.48 GHz to 64.80 GHz. ns-3 predicts 1.12 ms latency for this configuration, inside the 1.5 ms SLA, so it passes gate 1 of the pre-flight check.

## Slide 8
ADAPTER ③ · TFS → HARDWARE
Stage → verify → commit, with automatic rollback
STAGE 1
Stage the candidate
Decision engine output becomes YANG config
Held in the TFS candidate datastore, not live
Diff checked against the running config
STAGE 2 · TS 28.561
Pre-flight gates
Latency 1.12 ms ≤ 1.5 ms
Buffer occupancy < 40%
MH-T261 supports MCS 4
64.80 GHz inside V-band mask
STAGE 3 · RESTCONF
Two-phase commit
Prepare: PATCH the candidate
Commit: POST ietf-netconf:commit
Verify: poll telemetry
Health check fails → automatic rollback
Zero-outage by design: bad configurations are rejected in software before they can touch customer traffic.
Notes: Stage 1, candidate datastore staging: the AI decision engine output is translated into YANG configuration and staged in the TeraFlowSDN candidate datastore. Target device: Ceragon MH-T261 (UUID f676623c...). Changes: ACM floor MCS 0 -> MCS 4 (>= 500 Mbps), QoS FIFO -> IEEE 802.1Q PCP class 6 (PfifoFast), carrier 60.48 GHz -> 64.80 GHz. Stage 2, pre-flight safety gate (3GPP TS 28.561): gate 1 latency (predicted 1.12 ms <= 1.5 ms), gate 2 queue stability (buffer occupancy < 40%), gate 3 hardware capability (MH-T261 supports MCS 4), gate 4 spectral mask (64.80 GHz approved in V-band). Stage 3, two-phase commit over RESTCONF to 192.168.1.225:80: phase 1 PATCH the candidate datastore, phase 2 POST ietf-netconf:commit, then continuous RFC 8040 telemetry polling with automatic revert if health checks fail.

## Slide 9
END-TO-END
One closed loop, seconds instead of hours
≈ 2 s
per loop
1 Intent
TMF921
2 Simulate
ns-3 what-if
3 Verify
TS 28.561 gates
4 Actuate
RESTCONF 2PC
5 Monitor
live telemetry
Where the ~2 s go
1.15 s
+0.3
0.75 s
ns-3 what-if (Tier 4)
reconcile · verify · commit
hours
manual CLI troubleshooting
1.9–2.2 s
autonomous closed loop
Notes: The loop: SLA intent is ingested (TMF921), simulated in ns-3, safety-verified against the TS 28.561 gates, actuated through TeraFlowSDN over RESTCONF, and monitored through live telemetry. End to end this takes about 1.9 to 2.2 s. The ns-3 what-if run at Tier 4 is about 1.15 s of that; the remaining 0.75-1.05 s is topology reconciliation, gate checks and the two-phase commit (derived as total minus simulation time). This replaces hours of manual CLI troubleshooting.

## Slide 10
SUMMARY
What the adapters deliver
Zero-risk what-if
Surges, rain fade and fibre cuts are tested in a µs-accurate twin, never on live circuits.
Multi-vendor, open
TMF921, 3GPP TS 28.561, ITU-T Y.3090, RESTCONF/YANG: no proprietary lock-in.
Seconds-scale self-healing
Intent to verified change in ≈2 s, replacing hours of manual CLI work.
ADAPTER | TRANSLATES | STANDARD
① Intent | Natural language / SLA bounds → TFS service & CSPF requests | TM Forum TMF921
② Simulation | Live TFS graph → scoped ns-3 run → µs traces | TS 28.561 · Y.3092
③ Southbound | Candidate diff → gated two-phase commit on MH-T261 | RFC 8040 / 7950
Notes: Zero-risk what-if validation: operators test severe perturbations (3.5x bulk surges, category-5 tropical rain fade, fibre cuts) in a microsecond-accurate twin without risking live production circuits. Standardised multi-vendor interoperability: built on open telecom specifications (TMF921, 3GPP TS 28.561, ITU-T Y.3090, ITU-T Y.3092, RFC 8040 RESTCONF) with the open-source ETSI TeraFlowSDN controller. Seconds-scale closed loop: SLA intent is ingested, simulated, verified and actuated in about 1.9-2.2 s. (The original deck called this 'sub-second'; the measured end-to-end figure is about 2 s.)